## Slide 1
Multi-Site Solar
Irradiance Forecasting
Time Series Analysis — Master's Final Project
Ferran Dalmau Codina & Christopher Perry
Universitat de Barcelona · 2025–2026

## Slide 2
Agenda
1.
Motivation & Problem Statement
2.
Data Source & Station Network
3.
Clearsky Index & Feature Engineering
4.
SARIMA Baseline
5.
SolarGRU Architecture
6.
SolarGNN Architecture
7.
Training Setup
8.
Results & Model Comparison
9.
Conclusions & Future Work

## Slide 3
Why Solar Forecasting?
Solar energy is intermittent. Grid operators need accurate GHI forecasts
to balance supply and demand and reduce curtailment costs.
30%
EU electricity from
renewables (2024)
3
Forecast horizons:
1 h, 6 h, 24 h ahead
GHI
Global Horizontal
Irradiance (W/m²)

## Slide 4
Problem Statement
Goal
Forecast GHI at a target station in central Spain
(41.93°N, near Valladolid) at 1 h, 6 h, and 24 h ahead.
Key Insight
Clouds are the main source of error — and clouds move.
A station to the west can "see" an incoming cloud front
before it reaches the target.
→ Multi-site models exploit this spatial signal
Target
☁ →
Cloud movement
Neighbour stations (grey)
provide early warning

## Slide 5
Data Source
NREL NSRDB — National Solar Radiation Database
Typical Day Year (TDY) CSVs, hourly resolution
Multiple weather stations across Spain
Variables: GHI, Clearsky GHI, Cloud Type, Temperature, Humidity, Wind, Pressure
Target station near Valladolid (41.93°N, −4.26°W)
Neighbour stations provide spatial context for cloud movement

## Slide 6
The Clearsky Index
kt = GHI / Clearsky GHI
kt ≈ 1
Perfectly clear sky
kt < 0.5
Cloudy conditions
kt = 0
Nighttime (no solar radiation)
Removes the deterministic astronomical cycle (sunrise/sunset, seasons).
The model focuses only on cloud variability — the hard part.

## Slide 7
Feature Engineering
Feature
Description
kt (clearsky index)
Target variable and lagged input
Cloud Type
NSRDB classification (0–12)
Temperature, Dew Point
Surface meteorology
Humidity, Pressure
Atmospheric conditions
Wind Speed + sin/cos(dir)
Wind as unit-vector encoding
Solar Zenith Angle
Sun position (geometric)
sin/cos(hour), sin/cos(doy)
Cyclical temporal encodings
All features standardised with training-split statistics — no data leakage.
Neighbour stations use a reduced 6-feature subset to avoid overfitting.

## Slide 8
Three Modeling Approaches
SARIMA
Statistical baseline
Per-horizon direct forecast
SARIMA(1,0,1)(1,1,1)[24]
Fit window scales with horizon
SolarGRU
Deep learning
Separate GRU encoder per site
Fused before prediction head
~49k parameters
SolarGNN
Graph neural network
Stations = graph nodes
Edge weights from distance
~47k parameters

## Slide 9
SARIMA — Statistical Baseline
SARIMA(1, 0, 1)(1, 1, 1) [s = 24]
Direct forecast strategy: one separate SARIMA per horizon (1 h, 6 h, 24 h).
Short-horizon error never compounds into long-horizon estimates.
Horizon
Fit Window
1 hour
30 days
6 hours
60 days
24 hours
120 days

## Slide 10
SolarGRU — Architecture
Target Station
14 features
→
GRU
Encoder
→
Concat
& Fusion
→
Prediction
Head
→
kt at
+1h / +6h / +24h
Neighbour Stations
6 features each
→
GRU
Encoder
↑
~49,000 parameters · 24 h lookback window · Reduced features for neighbours avoid overfitting

## Slide 11
SolarGNN — Architecture
Edge weight:
w_ij = exp( −d²_ij / σ² )
d_ij = Haversine distance (km)
σ = 100 km (spatial decay bandwidth)
Close stations → high edge weight
Distant stations → low edge weight
New stations auto-adapt via kernel
Pipeline
1.
2× GCN layers → spatial aggregation
2.
GRU → temporal encoding
3.
Prediction head → kt at +1/+6/+24 h
~47,000 parameters

## Slide 12
GNN vs GRU — Why Graph?
SolarGRU
SolarGNN
Neighbour handling
Concatenate features
(treats all equally)
Graph message passing
(distance-weighted)
Topology awareness
None
Full — Gaussian kernel
New stations
Manual code changes
Auto-adapts via graph
Parameters
~49,000
~47,000

## Slide 13
Training Configuration
Loss
MSE — daytime steps weighted ×2
Optimiser
Adam (lr = 1e-3, weight decay = 1e-4)
LR Schedule
ReduceLROnPlateau (factor 0.5, patience 5)
Early Stopping
Patience 15 epochs
Lookback
24 hours
Batch Size
64
Data Split
70% train / 15% val / 15% test (chronological)
Train 70%
Val 15%
Test 15%

## Slide 14
Evaluation Metrics
MAE
Mean Absolute Error on kt
Σ|ŷ − y| / n
RMSE
Root Mean Squared Error on kt
√(Σ(ŷ − y)² / n)
nRMSE
RMSE normalised by mean observed kt
RMSE / mean(y)
Skill Score
Improvement over persistence baseline
1 − RMSE_model / RMSE_pers
R²
Coefficient of determination
1 − SS_res / SS_tot

## Slide 15
Results — Update With Your Data
Replace the values below with your comparison_metrics.csv results:
Model
Horizon
MAE
RMSE
nRMSE
Skill
R²
SARIMA
1 h
___
___
___
___
___
SARIMA
6 h
___
___
___
___
___
SARIMA
24 h
___
___
___
___
___
SolarGRU
1 h
___
___
___
___
___
SolarGRU
6 h
___
___
___
___
___
SolarGRU
24 h
___
___
___
___
___
SolarGNN
1 h
___
___
___
___
___
SolarGNN
6 h
___
___
___
___
___
SolarGNN
24 h
___
___
___
___
___
Tip: open comparison_metrics.csv from the repo and paste in the actual values

## Slide 16
Results — Visual Comparison
Update the chart series below with your actual metric values:
Chart: MAE by Horizon (update values)
| 1 h | 6 h | 24 h
SARIMA | 0.15 | 0.28 | 0.35
SolarGRU | 0.08 | 0.18 | 0.25
SolarGNN | 0.07 | 0.17 | 0.24

## Slide 17
Key Findings
1
Multi-site models significantly outperform single-site SARIMA
by exploiting spatial cloud-movement information.
2
SolarGNN slightly edges out SolarGRU on most metrics,
and scales better with new stations (no code changes needed).
3
Predicting kt instead of raw GHI removes astronomical noise —
the model focuses on what matters: cloud variability.
4
1 h predictions are very accurate; 24 h ahead remains hardest
due to chaotic cloud dynamics.

## Slide 18
Future Work
More stations
Expand the network across the Iberian Peninsula.
Attention mechanisms
Replace GCN with graph attention (GAT) for dynamic edge weights.
Probabilistic forecasts
Quantile regression or mixture density networks for uncertainty.
Real-time deployment
API serving live predictions with streaming NSRDB data.

## Slide 19
Thank You
Questions & Discussion
Ferran Dalmau Codina & Christopher Perry
github.com/U150401/timeseries-solar-irradiance